Hunter 41 Bimini Installation Instructions

You will need several 3/16” drill bits and a strong drill.  Drilling through stainless arch is not easy.  Your first step is to install the awning track (provided) on top of the arch (see photo #1).

Start by pre-drilling the holes in the awning track. 1” from the ends, then evenly space the center holes.

With the awning track laying flat on top of the arch, mark the holes that you drilled into the awning track through to the arch. Then drill the holes into the arch tubing, secure the awning track with the 3/16” rivets (provided).

Once both pieces of track have been installed forward and aft you can start on the mounts. We now use clamp on Jaw Slides.  Now you simply clamp on the mounts making for a cleaner, easier, and better looking installation. Mount locations will still be found by measuring from the top of the arch mount bracket.

Measurements are as follows:

Forward mount 32 1/2” & aft mount 47”.

Next you will find six jaw slides for ease of installation on your new frame, (2) for the fwd (2) for the aft frame, and (2) for the stiff legs

Next install both frames by putting the eye ends on the frames into the jaw slides. Slide the canvas onto the awning track and zip on the canvas to the frame.

After the canvas is put on the frame, hold the edges (next to the arch) and mark where the snaps go. (There should be four to five on each side) Then drill the holes using a ¼” drill bit and attach the cloth studs to the arch with the 1/8” rivets provided, then match the studs on the arch to the canvas, and put the snaps on the canvas. Next put the jaw slides for the stiff legs on the fwd arch tubing, towards the top (see photo) and attach the eye end to the jaw slide.

Adjust by pulling down on the front of the frame. Then tighten the jaw slide down.

Please refer to the photographs often as reference.  Please don’t hesitate to call if you need assistance!

41  Hunter Hardware List:

- 4 CLAMP ON JAW SLIDES

- 2 D-RING STRAPS

- 2 BIMINI STRAPS

- 10 3/16 STAINLESS STEEL RIVETS

- 2 PIECES OF ALUMINUM AWNING TRACK

- 20 1/8” RIVETS

- 20 CLOTH STUDS

# INSTALLING THE TRACK

# FORWARD MOUNT 32 1/2”     AFT MOUNT 44”

# SNAPS ON ARCH & STIFF LEG MOUNTS

Snaps on top of arch